# City of Melbourne Design Standards

## Barbecue - double 707.03

Date issued: 07.01.2014

The double BBQ is used in parks and gardens outside the Central City.

Ideally, the BBQ should be positioned near picnic table sets.

For BBQs located within Docklands, the body is fabricated from grade 316 stainless steel, elsewhere they are fabricated from galvanised steel and powder coated Dulux ‘Deep Brunswick Green’ 6134G. The bench is top grade 316 stainless steel sheet.

### Section

### Plan

Concrete Slab is to be ‘Charcoal’ coloured, achieved by adding 15kg/m3 black oxide ‘Bayer 318’, or approved equal, to concrete mix prior to pouring.

For fabrication and installation drawings, refer to City of Melbourne, City Design drawings: Project No. 900861_F_Double_BBQ_Fabrication-130612 and 900861_F_Double_BBQ_Fabrication-130515.