# City of Melbourne Design Standards

## Bicycle Hoop 706.08

Date issued: 07.01.2014

Bicycle hoops are used throughout the municipality.

Bicycle hoops are located within footpaths along cycle routes, cycle destination points or public attractors.

Bicycle hoops should be installed in groups of two or more. They should be spaced one metre apart and offset a minimum of 800mm from the face of kerb, building or walls. The hoops can be placed at an angle of 90, 60, 45 or 30 degrees so as not to impede pedestrian access along footpaths.

Bicycle Hoops are fabricated from 316 grade stainless steel and polished to a 'No. 4' satin polish.

For fabrication drawings, refer to City of Melbourne, City Design drawings; Project No: 5084_F01_Bike Hoop-Fabrication_130530.

For fabrication drawings, refer to City of Melbourne, City Design drawings; Project No: 5084_F01_Bike Hoop-Fabrication_130530.Plan – bike hoops parallel to kerb

### Plan – bike hoops angled to kerb

### Section