# City of Melbourne Design Standards

## Barbecue - single 707.02

Date issued: 07.01.2014

The single BBQ is used in parks and gardens outside the Central City.

Ideally, the BBQ should be positioned near picnic tables.

For BBQs located within Docklands, the body is fabricated from grade 316 stainless steel, elsewhere they are fabricated from galvanised steel and powder coated Dulux ‘Deep Brunswick Green’ 6134G. The bench is top grade 316 stainless steel sheet.

### Section

### Plan

Concrete Slab is to be ‘Charcoal’ coloured, achieved by adding 15kg/m3 black oxide ‘Bayer 318’, or approved equal, to concrete mix prior to pouring.

For fabrication and installation drawings, refer to City of Melbourne, City Design drawings: Project No. 5105_F_BBQ_single_fabrication_130612 & 5105_F-BBQ_single_installation_130516.